## Slide 1: JPEG Encoder
Credit : students
Digital Design 2007

## Slide 2: How to run ?
Assuming Modelsim simulator
  do modelsim_run_file
Take the resulting *hex file and convert it to bmp with hex2bin.rb

## Slide 3: Top Level Architecture
imager
flash disk
JPEG encoder system
shoot task

## Slide 4: Imager I/O
pin name | width | direction | description
rst | 1 | input | reset the device, active high
clk_in | 1 | input | clock input. 12.5Mhz
file_name | 128 | input | the hex file's name
shoot | 1 | input | instruct the imager to take a new picture
vid_type | 1 | input | 1 for RGB, 0 for YUV (we didn’t implement the YUV option).
hd | 1 | output | synch for horizontal data
vd | 1 | output | synch for vertical data
pxq | 1 | output | pixel qualifier
dout | 8 | output | pixels output data

## Slide 5: Encoder
Parser
Buffer
Encoder Block Diagram
DCT &
Quantization
ZIG ZAG
Huffman
FIFO
Flash
Writer
DCT
Quan

## Slide 6: Encoder
Encoder I/O
pin name | width | direction | description
rst | 1 | input | reset the device, active high
clk_in | 1 | input | clock input. 100Mhz
shoot | 1 | input | instruct the encoder to start writing the header
file_name | 160 | input | the output file name
factor_sel | 2 | input | the quality factor we chose for the picture (0=25, 1=50, 2=75, 3=100)
date_string | 64 | input | the string with the date
print_date | 1 | input | signal that implicates whether to print the date or not (active high)
pxq | 1 | input | pixel qualifier from imager
d_in | 8 | input | the data from the imager
s_halt | 1 | input | halt from the flash disk
qual2flash | 1 | output | data qualifier to the flash disk
data2flash | 32 | output | write data to flash disk
be2flash | 4 | output | byte enable to flash disk
m_cmd | 2 | output | always equal to 2’b10 (indicates WRITE to the flash disk)
m_halt | 1 | output | inserts NOP on the line to the flash disk
eof2flash | 1 | output | end of file to flash disk

## Slide 7: Encoder
PARSER
I/O
pin name | width | direction | description
rst | 1 | input | reset the device, active high
clk_in | 1 | input | clock input. 100Mhz
pxq | 1 | input | pixel qualifier from imager
d_in | 8 | input | the data from the imager (integer)
print_date | 1 | input | signal that implicates whether to print the date or not (active high)
date_string | 64 | input | the string with the date
line_width | 32 | Output | Line width, in pixels.
pic_height | 32 | Output | Picture height, in pixels.
dimensions_valid | 1 | Output | Orders the header_writer to write the size of the picture.
d_qual | 1 | Input | halt from the flash disk
dout | 8 | Output | Output data to the buffer.

## Slide 8: Encoder
Parser
receives the data from the imager
parses the file name and data in the encoder clock domain
Transforms RGB to YCbCr
Inserts the date if necessary

## Slide 9: Encoder
BUFFER
I/O
pin name | width | direction | description
rst | 1 | Input | reset the device, active high
clk_in | 1 | Input | clock input. 100Mhz
rd | 1 | Input | Order the buffer to put next data on the bus.
wr | 1 | Input | Order the buffer to store ‘wr_data’ in the buffer.
wr_data | 8 | Input | Input data (integer).
line_width | 32 | Input | Line width, in pixels.
pic_height | 32 | Input | Picture height, in pixels.
rd_data | 8 | Output | Output data to DCT.
valid | 1 | Output | Output data qualifier.

## Slide 10: Encoder
Buffer
Two redundant buffers that receive YCbCr data from the parser and saves it in one of them, while previous data being read from the other by the DCT (Ping Pong).
The input data is being saved according to the YCbCr and the number of block. The data is being read in sequential order every time ‘read’ signal is high.

## Slide 11: Encoder
DCT & Quantization
I/O
pin name | width | Direction | description
rst | 1 | Input | reset the device, active high
clk_in | 1 | input | clock input. 100Mhz
rd_data | 8 | Input | Input data from the buffer (integer).
Valid | 1 | Input | Validity of the received data (active high).
factor_sel | 2 | Input | Q factor of the picture (0=25, 1=50, 2=75, 3=100)
zig_zag_wr_addr | 6 | Output | Output data address in the Zigzag ram.
zig_zag_wr_en | 1 | Output | Write enable signal for the Zigzag ram.
d_out | 12 | Output | Data out to store in the Zigzag ram (integer).
rd | 1 | Output | High when data in the input stream can be changed.
eof | 1 | Output | High after processing the entire file, low else (pulse).
max_not_zero_idx | 6 | Output | The index of the last non zero value.

## Slide 12: Encoder
DCT & Quantization
DCT I/O
pin name | width | direction | description
rst | 1 | input | reset the device, active high
clk_in | 1 | input | clock input. 100Mhz
d_in | 24 | Input | Input data from the buffer (fp).
valid_d_in | 1 | Input | Validity of the received data (active high).
Valid_d_out | 1 | Output | Validity of the d_out.
d_out | 24 | Output | Data to quantization (fp).
rd | 1 | Output | High when data in the input stream can be changed.
eof | 1 | Output | High after processing the entire file, low else (pulse).

## Slide 13: Encoder
DCT & Quantization
Quantization I/O
pin name | width | Direction | Description
rst | 1 | Input | reset the device, active high
clk_in | 1 | input | clock input. 100Mhz
d_in | 24 | input | The received data (fp).
valid_d_in | 1 | Input | Validity of the received data (active high).
factor_sel | 2 | Input | Q factor of the picture (0=25, 1=50, 2=75, 3=100)
eof_in | 1 | Input | Notifies the unit that the input data has ended (pulse).
zig_zag_wr_addr | 6 | Output | Output data address in the Zigzag ram
zig_zag_wr_en | 1 | Output | Write enable signal for the Zigzag ram
d_out | 12 | Output | Data out to store in the Zigzag ram
Rd | 1 | Output | High when data in the input stream can be changed.
eof_out | 1 | Output | High after processing the last input (pulse).
max_not_zero_idx | 6 | Output | The index of the last non zero value in the block.

## Slide 14: Encoder
DCT & Quantization
Reads the data from the buffer when gets ‘valid’ from it.
Calculates the Discrete Cosine Transform of each block.
Multiply each value in the DCT matrix with the quantization factor respectively.
Outputs the data towards the zig-zag RAM as 12’bit integer with the appropriate address.

## Slide 15: Encoder
DCT & Quantization
Notes
The throughput of each block is 512 cycles for DCT and one quantization cycle.
Uses single ROM for the DCT values.
Quantization’s ROM contains 4 different data sets according to the 4 available quality factors.
In order to prevent complex division, the quantization ROM holds inverse data.

## Slide 16: Encoder
Zig-Zag
I/O
pin name | width | Direction | Description
rst | 1 | Input | reset the device, active high
clk_in | 1 | input | clock input. 100Mhz
d_in | 12 | Input | Input data from the quantization (integer)
zig_zag_wr_en | 1 | Input | Write input data
zig_zag_rd_en | 1 | Input | Read next data
zig_zag_wr_addr | 6 | Input | Write address in Zigzag ram
zig_zag_rd_addr | 6 | Input | Read address in Zigzag ram
eof_in | 1 | Input | High when the quantization unit finished to process the entire file (pulse).
halt | 1 | Output | Prevents the Huffman unit from reading next data while the quantization units writing new data.
Zig_zag_rd_data | 12 | Output | Output data to the Huffman unit.
huffman_start | 1 | Output | Order the Huffman to start reading new block (pulse).
eof_out | 1 | Output | High after processing the entire file, low else (pulse).

## Slide 17: Encoder
Zig-Zag
Uses single port RAM.
Receives the data and address from the previous block every 8 cycles and writes it to the RAM.
Data can be read during the remaining cycles.

## Slide 18: Encoder
Huffman
pin name | width | Direction | description
rst | 1 | Input | reset the device, active high
clk_in | 1 | input | clock input. 100Mhz
start | 1 | Input | Trigger to read and process new block (pulse).
zig_zag_halt | 1 | Input | High when zig-zag is busy and can’t deliver new data.
fifo_full | 1 | Input | High when the fifo is full.
eof_in | 1 | Input | High when the zig-zag unit finished to deliver the entire file (pulse).
ram_d_in | 12 | Input | Data in from the zig-zag (integer).
max_not_zero_idx | 6 | Input | The index of the last non zero value in the block.
ram_rd | 1 | Output | Request new data from the zig-zag.
eof_out | 1 | Output | High after processing the entire file, low else (pulse).
ram_addr | 6 | Output | The address to read from the zig-zag.
d_out | 33 | Output | Output data stream to the flash writer. [32:28] valid bits number, [27:0] data bits.
d_qual | 1 | Output | Data qualifier.

## Slide 19: Encoder
Huffman
Holds 4 ROM tables (AC-Lum, DC-Lum, AC-Chrom, DC-Chrom).
Reads from the Zig-Zag RAM in sequential order.
Translates the data according to the Huffman algorithm (counting zeros, calculating category of each data, reads the appropriate address from the ROMs).
Receives from the quantization the address of last non-zero value (after reading the data of this address, writes EOB symbol).

## Slide 20: Encoder
FIFO
I/0
pin name | width | Direction | description
rst | 1 | Input | reset the device, active high
clk | 1 | input | clock input. 100Mhz
rd | 1 | Input | Read enable trigger.
wr | 1 | Input | Write enable trigger.
wr_data | 33 | Input | Input data.
full | 1 | Output | Indicates that the fifo is full.
empty | 1 | Output | Indicates that the fifo is empty.
rd_data | 33 | Output | Output data.

## Slide 21: Encoder
FIFO
Buffers the data from Huffman in order to synchronize the writing mechanism to the flash disk.
The purpose of this FIFO is to make the following possible:
  Receiving ‘halt’ signals from the flash disk
  Writing header to flash disk
  Padding ‘ff’ bytes with zeros

## Slide 22: Encoder
FLASH WRITER
I/O
pin name | width | Direction | description
rst | 1 | Input | reset the device, active high
clk_in | 1 | input | clock input. 100Mhz
fifo_empty | 1 | Input | Indicates that the fifo is empty.
halt | 1 | Input | Indicates that the flash disk is busy and temporally can not handle new writes.
eof_in | 1 | Input | Huffman unit reached end of file (pulse).
stream_in | 28 | Input | Huffman code data stream.
stream_in_size | 5 | Input | The number of valid bits in stream_in.
flash_data | 32 | Output | Output data to flash memory.
fifo_rd | 1 | Output | Request new data from the fifo.
flash_stop | 1 | Output | Prevents the flash disk from writing new data.
eof_out | 1 | Output | High after writing the eof symbol to the disk (pulse).
byte_en_mask | 4 | Output | Output validity bytes mask.

## Slide 23: Encoder
Flash Writer
Writes the header of the file after ‘shoot’ signal.
Reads the 33’bit data from the FIFO (28’bits Huffman stream and 5’bits size).
Aliens the data in 4 byte chunks and outputs it to the flash disk.

## Slide 24: Flash Disk I/O
pin name | width | direction | description
rst | 1 | Input | reset the device, active high
clk_in | 1 | Input | clock input. 100Mhz
m_cmd | 2 | Input | master command, 00 for NOP, 01 for READ, 10 for WRITE
d_qual | 1 | Input | Input data qualifier.
m_be | 4 | Input | Input bytes validity mask.
m_halt | 1 | Input | Halts the flash disk.
m_eof | 1 | Input | Indicates that the master reached eof and orders the flash disk to close the file (pulse).
d_inout | 32 | Inout | Data input/output bus.
s_be | 4 | Output | Output bytes validity mask.
err | 1 | Output | Indicates internal error in the flash disk.
s_halt | 1 | Output | Indicates that the flash disk is busy, halts the slave.
s_eof | 1 | Output | Verifies that the flash wrote the entire file and closed it.

## Slide 25: The result
Quality factor = 25 (5.77Kb)
Quality factor = 50 (4.14Kb)
Quality factor = 75 (3.52Kb)
Quality factor = 100 (2.99Kb)
Original BMP picture (26.8Kb)